## Slide 1: TCP connection

## Slide 2
TCP is connection-oriented.
It establishes a virtual path between the source and destination.
All of the segments belonging to a message are sent over this virtual path.
TCP, which uses the services of IP, a connectionless protocol, can be connection- oriented.
The point is that a TCP connection is virtual, not physical.
TCP operates at a higher level.
TCP uses the services of IP to deliver individual segments to the receiver, but it controls the connection itself.
If a segment is lost or corrupted, it is retransmitted.
This protocol works based on full duplex mode.

## Slide 3
Connection establishment using three-way handshake

## Slide 4
Data transfer

## Slide 5
Connection termination using three-way handshaking

## Slide 6
TCP Window Management (Control Flow)
TCP uses two windows (send window and receive window) for each direction of data transfer, which means four windows for a bidirectional communication
To make the discussion simple, we make an assumption that communication is
only unidirectional
The bidirectional communication can be inferred using two unidirectional communications with piggybacking

## Slide 7
Send window in TCP

## Slide 8
Receive window in TCP

## Slide 9
Sliding window
A sliding window is used to make transmission more efficient as well as to control the flow of data so that the destination does not become overwhelmed with data.
TCP sliding windows are byte-oriented

## Slide 10
What is the size of the window for host A if the value of rwnd is 3000 bytes and the value of cwnd is 3500 bytes?
Solution
The size of the window is the smaller of rwnd and cwnd, which is 3000 bytes

## Slide 11
Normal operation

## Slide 12: Lost segment

## Slide 13
Fast retransmission
The receiver TCP delivers only ordered data to the process

## Slide 14
UDP
The User Datagram Protocol (UDP) is called a connectionless, unreliable transport protocol
It does not add anything to the services of IP except to provide process-to process communication instead of host-to-host communication

## Slide 15
Well-known ports used with UDP

## Slide 16: UDP format

## Slide 17
Pseudo-header for checksum calculation

## Slide 18
UDP provides
  best effort delivery
  Connectionless
  Unreliable
  Out of order delivery
TCP
  Reliable
  In-order delivery
  Congestion control
  Flow control
  Connection setup